$NOME
Manuale Software

MAREL srl - FABRIANO (AN) – Italy
www.marelsrl.com

# GasTapsEnhTestSystem
This manual describes the procedures for the proper use of the software GasTapsEnhTestSystem supplied with the taps test system .
## Taps test system
This system has been designed and developed for the acquisition of values of torque, pressure and temperature of the taps during the rotation in the two directions: anticlockwise and clockwise.
During the testing phase the torque curves detected are plotted and are saved components with peak values over a maximum threshold set. The system can also automatically perform leak testing of valves and magnets .
For each slot, the system is further equipped with four digital inputs for reading as many contacts during the phases of handling.
## Settings and configuration
This chapter describes how to install and configure the program and acquisition of all components and drivers necessary.
The system supplied to the customer, is already working so this procedure should not be performed.

The information contained in this section are helpful only for a possible replacement of the PC or in the case of a new installation of the operating system Windows XP / Windows 7.
### Installing the acquisition card ADVANTECH
Based by the software version the Advantech driver used are different. For the software release over the 1.6.0 it's necessary to install the Advantech DaqNavi otherwise are required the old legacy driver supplied with the Advantech Device Manager.
#### Advantech Device Manager driver
Before inserting the card ADVANTECH PCI 1716 you must install the driver Advantech.

The drivers are automatically installed with the setup program as described in the next paragraph. When the installation is completed, you can turn off the computer to insert the card. After restart of the computer, proceed with the setup of analog channels via the program Advantech Device Manager specifying the mode “single-ended” or “differential” (*).
#### Advantech DaqNavi driver
There is no specific steps to follow to install the newest version of the driver. Simply follows the on screen instruction once started the procedure. Also the configuration of the channels is performed by the software each time it's starts.
### Application installation
The procedure for installing the program is as follows:
1. Insert the installation CD-ROM supplied with the system in the CD player;
2. Start the setup program Setup GasTapsEnhTestSystem x.xx;
3. Leave the default settings and wait for the completion of the installation procedure.
Program settings (serial port connected to the oven/climatic chamber , the header of the client etc …) are shown in a configuration file as described in the next paragraph.
### Application configuration
During the installation automatically creates the configuration file GasTapsEnhTastSystem.exe.config with the correct settings. However if you need to make some changes (customer name, serial communication etc …) you can open the file with any text editor such as Windows Word Pad.
The content of the file is as follows:
<?xml version="1.0" encoding="utf-8"?>
<configuration>
  <startup>
    <supportedRuntime version="v4.0" sku=".NETFramework,Version=v4.5" />
  </startup>
   <appSettings>
     <!--lingua utilizzata nell'applicazione:it,ro,pl-->
     <add key="LINGUA" value="it"></add>
     <!--seriale di comunicazione con forno/camera climatica (""=non collegato)-->
     <add key="COMM_FORNO" value=""></add>
     <!--tipo forno-->
     <add key="TIPO_FORNO" value="0"></add>
     <!--indirizzo ip del forno/camera climatica (""=non collegato)-->
     <add key="IP_ADDRESS_FORNO" value="192.168.100.100"></add>
     <!--seriale di comunicazione con le PM110 (""=non collegate)-->
     <add key="COMM_PM110" value="4"></add>
     <!--ID della scheda advantech. Vedere advantech DaqNavi (-1=disabilitata)-->
     <add key="ID_SCHEDA_ADVANTECH" value="-1"></add>
     <add key="ADVANTECH_AI_DIFFERENZIALI" value="1"></add>
     <!--seriale moduli TC/AO-->
     <add key="COMM_MODULI_TC_AO" value=""></add>
     <!--modulo ingressi termocoppie (tttt:ADAM_4018,ICPDAS_7018Z. ""=non collegato)-->
     <add key="TIPO_MODULO_TC" value=""></add>
     <!--movimantazione assiale-->
     <add key="MOVIMENTAZIONE_ASSIALE" value="1"></add>
     <!--1=abilita la lettura degli ingressi-->
     <add key="INGRESSI_ABILITATI" value="1"></add>
     <!--generalità del cliente e nome sistema-->
     <add key="CLIENTE" value="MAREL srl"></add>
     <add key="SISTEMA" value="GAS TAPS ENH TEST SYSTEM"></add>
     <!--"0"=non presente, 1=solo lettura (secondo ingresso Analogico), 2=lettura e regolazione (specificare la seriale in COMM_MODULI)-->
     <add key="REGOLAZIONE_PRESSIONE" value="0"></add>
     <!--posizione prima postazione("DX" o "SX")-->
     <add key="POSIZIONE_PRIMA_POSTAZIONE" value="DX"></add>
     <!--postazioni per colonna-->
     <add key="POSTAZIONI_COLONNA" value="2"/>
     <!--presenza braccetto apertura porta 0=no, 1=normale, 2=con sblocco-->
     <add key="APERTURA_FORNO" value="1" />
     <!--secondi impiegati nella movimentazione della porta-->
     <add key="TEMPO_APERTURA_FORNO" value="12" />
     <!--presenza ventola supplementare di raffreddamento-->
     <add key="VENTOLA_FORNO" value="1" />
     <!--presenza resistenza supplementare di riscaldamento-->
     <add key="RESISTENZA_FORNO" value="1" />
     <!--seriale di comunicazione e dispositivo test tenuta ATEQ/FORTEST (modalità demo = 0,DEMO)-->
     <add key="COMM_TIPO_TENUTA" value="" />
     <!--controllo rotazione massima nello stesso senso-->
     <add key="ROTAZIONE_360" value="1" />
  </appSettings>
</configuration>
Be very careful not to change the file format, some special characters or spaces accidentally inserted may affect the startup testing and operation of the machine.

## Starting the program
To start the application, select the command Start » Programs » MAREL » GasTapsEnhTestSystem or double-click on the desktop icon GasTapsEnhTestSystem.

Icona "GasTapsEnhTestSystem" nel desktop
## Select language
In the menu , select File »Language and then click with the mouse in the corresponding to the desired language:
“It” = Italian, “ro” = Romanian, “pl” = Polish, “en” = English …
The selected language will be activated on the next restart of the application.
The list of available languages varies according to the translation files ”.po” in the program folder.

## Close application
Select File » Exit from the menu or ALT + F4 or simply the following button in the toolbar:

click on Yes button or press ENTER to the next confirmation message.
You cannot end the program with a test active. In this case if there is in course a the movement , the program awaits the completion.

# User interface
Main screen is as follows:

Schermata principale
The top bar displays the title of the application and contains three buttons for resizing and closing the program (refer to the operating system installed on your computer).
Are located immediately below the Menu bar and Toolbar.
On the left there is the List places and tests and oven/climatic chamber panel.
Depending on your selection in the list of places, in the center of main screen will be displayed the Panel places or the Graphic area.
The statusbar placed in the bottom of the window, displays the current date and time without necessarily show the standard applicationbar of windows.
## Menu bar
From the menu bar you can access all the functions provided by the test program. These functions can be selected with the mouse or keyboard, press the Alt key and then the underlined letter of the command chosen. The most-used can also be activated via a function key or a key combination as shown in the next menu.
The following table summarizes all the menu commands:
Commands Menu	Description	Shortcut
File
–> Events	See the list of recorded events	CTRL + L
–> Exit	Closes the application	ALT + F4
Archive
–> Components	View the components Database	F2
–> Advanced programs	View the advanced programs Database	F3
–> Standard programs	View the standard programs Database	F4
–> Tests	View the tests Database	F9
–> External tests	View the list of tests stored in another location or unit	ALT + F9
–> Close	Closes an open test from the archive	CTRL + C
–> Backup	Start the backup utility of tests
Test
–> New	Create a new test	CTRL + N
–> Repeat	Start a new test with the same settings as the last runned	CTRL + R
–> Modify	Change the setting of a test	CTRL + M
–> Start	Start / Resume a test	F5
–> Suspend	Suspend a test	F6
–> Suspend and unlock	Suspend a test and unlocks motors
–> Delete	Delete a test
–> Save	Save a test in the Database
–> Details	View details of the program of the selected place	CTRL + D
–> Value max	Displays the maximum values diagram	CTRL + V
–> Leakage test	Display a window with the list of leakage test performed	CTRL + T
–> Result	Displays the window for entering / editing a possible result	CTRL + E
Place
–> Calibrate	Displays the calibration of the torque for the selected place
–> Save and continue	Save the data of the place and continues testing with the remaining
–> Exclude and continue	Deletes data of the place and continues testing with the remaining
Instruments
–> Install components	Opens the panel for manual management of places	F8
–> Input calibrator	(optional) Opens the panel for the calibration of the thermocouples detection temperatures
–> Password	Enable / Disable functions administrator, password protected
Settings
–> Drawing	View / Edit graph settings	F10
–> Option	Opens the settings panel program	F11

## Toolbar
The toolbar contains buttons for quick access to some of the menu commands:
Icon	Icon Toolbar	Menu commands
	Close application	File–>Exit
	Enable / Disable password-protected functions	Tools–>Password
	View the archive of components	Archive–>Components
	View the archive of advanced programs	File→ Advanced Programs
	View the archive of standard programs	File→ Standard programs
	View Archive test	Archive → Test
	Closes an open testing archive	Archive → Close
	Create a new test	Test → New
	Start a new test with the same settings as the last run	Test → Repeat
	Editing the data of a test	Test → Edit
	Start / Resume a test	Test → Start
	Suspends a test	Test → Pause
	Pause a test and unlocks motors	Test → Pause and unlock
	Delete a test	Test → Delete
	Save a test in archive	Test → Save
	View details of the program of the selected place	Test → Details
	Opens the settings panel program	Settings → Options
	Opens the panel for manual management of a places	Tools → Install components
	Change the graph settings	Settings → Drawing option
	View the event log	File → Events

## List places and tests
The tree list displays the oven/climatic chamber and its places. Selecting the oven/climatic chamber , the program displays the “Panel places”, instead selecting a place displays its data with the list of acquired curves and graph acquisition eventually selected “Graphic Area”.

List of places and tests
Any other tests reopened from the archive are appended and are represented by a different image:

## Oven/climatic chamber panel
Information regarding the operation of the oven/climatic chamber are grouped in the following panel:

Oven/Climatic chamber panel
The humidity option and commands to set the humidity, are available only if the system is supplied with a climatic chamber. Also other buttons can be disabled if the climatic chamber or oven doesn't support particular function like : stat/stop buttons, automatic open/close door etc…

##### Read Temperature (°C)
Display the internal temperature detected by the sensor of the oven/climatic chamber.
##### Humidity read (%)
Display the internal humidity detected by the sensor of the climatic chamber.
##### Temperature and gradient set (°C)
The temperature threshold and the temperature gradient actually set up. They can be changed only if the Manual mode is selected.
##### Humidity and gradient set (%)
The humidity threshold and the humidity gradient actually set up. They can be changed only if the Manual mode is selected. With left button it's possible to enable or disable the humidity control.
##### State
It indicates the mode of operation and the status of the serial communication, accompanied by an icon corresponding .:
- ONLINE–AUTO;
- ONLINE–MANUAL;
- ERROR.
If you receive the error status in the box below there is also a description explaining the problem.
To learn about the key functions go to the section Oven/climatic chamber options.
## Panel places
The panel of the places provides an overview of system status while displaying all the pitches of testing:

Pannello delle postazioni
Above, common to all places,are displayed the date / Start time testing, the test description and test program. Just below for each location the informations displayed are:
* In the top left corner there is the number for the place and to the right a colored light and a label that indicate the status as summarized in the following table:
Status List Place
	EMPTY	Place not in testing
	OFF	Place with a test not in execution
	ON	Place with a test in execution
	ERR	Communication error with the hardware place

- Just below displays the supplier/type, model and sample / code / ANC relating to the component. Depending on the type of running program also shows the following details of the test:
  - Standard program: current step, total step, the current cycle, total cycles and absolute counter cycle running;
  - Advanced program: current block, total block, current command, total command and the command name running;
- Lower down you see an arrow pointing to the right or left , based on the last rotation performed. Just below ,the temperature of the detection and the pressure exerted on the component. To the right, a red icon or a green icon and labeled “OK”, “KO” indicating the presence of possible errors in the below data.
- In the graphics area displays the torque curve of the last executed command, there are two orange lines representing the maximum reached by the torque so the curve if it is not over-range will be saved as “OK” or “NOK” (Not Ok). In the clockwise direction of the maximum line it is orange while the other is gray, and so vice versa.
The pressure value is only visible if at the start of the test in the field Pressure (N) specify a value other than 0. It will be displayed in green if it is within the specified tolerance, otherwise red.

## Graphic Area
Selecting the list of test a single place, the program shows a list of the curves acquired and the graph of the measured values acquired:

Area grafica
In the top bar are shown the following keys:
Tools for the Graphic Area
	Displays all the curves acquired
	Displays all the curves measured counterclockwise
	Displays all the curves measured clockwise
	Displays the curves with higher pick value obtained during the rotation
	Select the wrong curves. While pressing the SHIFT + CTRL activates the delete function curves erroneously detected
	Cancel selection of the curves
	Print a report of selected curves
	Export as text format all the values of selected curves
	Save the graph displayed as image format JPEG
	Delete the points plotted on the graph

In the list, for each curve detected, there are visible the following information:
- the step number or the combination lock / command in the case of an advanced programming;
- the number of the cycle in reference to the step or block;
- detection time and date;
- the direction: O for clockwise rotation, A for counterclockwise rotation;
- the temperature detected at the end of rotation (*);
- the pressure measured at the end of rotation;
- the start of rotation (expressed in degrees);
- degrees done;
- the rotation speed (expressed in degrees per second);
- the type of curve that can be “Auto” for curves stored according to the settings of the testing program otherwise empty for other saved because with negative results;
- the maximum value of torque (Nm);
- result of the curve;
- the number of detected contacts (for input 1) in axial movement;
- the number of detected contacts (for the inputs 2,3,4) during the phase of rotation.
The curves with negative results, whether for exceeding the rated value in the detection of the torque or for problems in contacts, they are shown in red.
(*) The temperature will be the one read by the controller of the oven/climatic chamber or if it is present by a module extra (ADAM 4018) for the connection of additional thermocouples that can be connected to each location.

The bottom panel shows the curves relating to the testing in question. The scale of the torque expressed in Newtons or Kilograms is arranged vertically, the degree scale is drawn horizontally. Pressing the left button of the mouse, over the graphic,a point is inserted at that displays with the torque value detected (if enabled in the graphics settings, in brackets are visible degrees of location). Holding down the right button you can instead quickly reviewing the torque values that are displayed next to a vertical bar traced continuously at the mouse.

Esempio di stampa grafico
# Test
In this section we will explain all the operations that can be performed during the test phases: start, pause, resume, modify, deleting and saving.
## New
To begin the phase of rotation and acquisition of the torque we need to create a test. Select in the menu Test » New or hold the key CTRL+N; or simply, press the following button in the toolbar:

The program displays the interface for input of data relating to the test to be performed:

Finestra di avvio nuovo collaudo
We have to select the places on which the testing will be performed, then press on the icons of the taps in the upper panel to enable or disable. If necessary, but not required for the purposes of test, enter a description of the test and subsequently for each component include the following information: Supplier / Type, Model, Description, Rotation Left (degrees), Rotation Right, Torque max (Nm), Pressure (N), Pressure tolerance (N), Contacts axial and Rotation counters. To load data from the components archive, select all the locations listed in the list by clicking with the mouse in the column all and press load for access to the archive:

Archivio componenti
Choose the place in the list and press Select to go back to the pane of test start. Afterwards you can manually change the setting loaded for each place simply selecting the place in the components list. The other fields : Sample/Code/ANC, Stamping/Data production, Lot/Traceability and Note they must be inserted step by step.
In the end to select the test program (unique for all components), click the panel programs Standard or Advanced and press Load for access to the selection window.
Highlight it in the list of those present in the archive and press Select.For more information on program standard and advanced management see the relevant paragraphs in chapter Archivio.
Complete the procedure by pressing on Confirm or Cancel for abort the start.
The modification of some fields regarding the rotation, the pressure and the inputs is allowed only after being authenticated with password.

## Repeat
Finished a test you can start a new one with the same settings as the last program done. Select on Menu Test » Repeat or press the keys CTRL+R or, simply, press the following button on the toolbar:

As for the editing (see next paragraph), the program displays a window to enter or change any information that does not affect the operation of testing.
## Modify
Also during the test we can change the information of the program that do not go to affect the implementation of the test . Choose from the menu Test » Modify, or press CTRL+M, or press this button on the toolbar:

From the window that appears you can correct the personal data of place:Supplier/Type, Model, Description, Sample/Code/ANC, Stamping / Data production, Lot/Machine and Note Is not possible to edit: maximum torque, number of axial and rotation contacts , rotation degree (Sx and Dx),value of the pressure plate and relative tolerance, and the test program running. If the test is not yet started, you can also remove one or more places from it. You must press the mouse icon in the upper panel and respond Yes to the next confirmation message. The place will now be removed from the testing resulting empty.
## Start
Once you created a new test you have to start it . Select fromt the menu Test » Start or press F5 or, simply, press the following button on the toolbar:

Once started the testing, at the end of each rotation, the program shows the graph of the torque detected with values of temperature and pressure detected on the component. During the leakage test phase that can be performed on a place at a time, in correspondence of the component concerned, is displayed a bar and the time left for the acquisition.
The same function can be used to resume a previously interrupted test.
## Pause
If a test is paused, it suspend the acquisition of data that can be retrieved later. To pause a test you have to select the menu Test » Pause or press the F6 or, more simply, press the following button in the toolbar:

Then select Yes in the following confirmation message. Wait for the program, complete the step of moving to return the components to the position of initial zero.
During the execution of an advanced program it stops after running the last command of cyclic block

## Interruption with unlock motors
As for the function Interruption this also stops the testing and in addition also unlocks the motors. To suspend a test select the menu Test»Pause or press the next button in the toolbar:
Then select Yes in the following confirmation message. Wait for the program, complete the step of moving to return the components to the position of initial zero.
During the execution of an advanced programm , it stops after running the last command cyclic block

## Delete
The elimination of a test deletes all data. To do this you must select the menu command Test » Delete or simply press the next button in the toolbar:

Then press Yes in the following confirmation message.
A test if deleted can not be retrieved anymore, so pay close attention.

## Save
This function allows you to save in archive the test finished or interrupted. First, it is advisable to complete the insertion of data relating to the test and the results of test, so that once saved, it can be found easily with the research tools. Select the menu item Test » Save or, more simply, press the following button in the toolbar:

Select Yes in the following confirmation message.
## Details
You can at any time display the details of the program test running. You must first select one of the places in the list on the right, and then select from the menu Test » Details , or press the key Ctrl + D alternatively press the following button from the toolbar:

In the window that appears summarizes all the data of the test and in the case of standard program, all steps of the running program, while in the case of advanced program, block information and controls testing.
To return to the main screen, press the Exit button.
### Details standard program

Dettagli programma di test standard
For every step of the program are displayed:
- N.: Progressive number;
- N.C.: Number of total cycle;
- I.: Starting degree of rotation;
- F.: Ending degree of rotation;
- Degree/Sec.: Rotation speed;
- C. Mov. Axial: Every how many cycles is performed axial movement;
- C. Ril. Torque: Every how many cycles is checked the torque value;
- T. (°C): Temperature of setpoint of the oven/climatic chamber ;
- C.Release: Every how many cycles runs release;
- Wait: Waiting time at the end of the rotation before returning back to zero;
- Direction: Initial direction of rotation;
- Cont. axial: Contacts axial connected;
- Cont. rotation: Contacts rotation connected.
### Details advanced program

This window shows a list of blocks with the respective controls that characterize the current program. For each block next to the consecutive number (in brackets) and the name, show the number of cycles performed and the total. Immediately below lists all the commands in extended mode with the appropriate parameters enclosed in brackets. Icons to the left of each item indicate the current state of the program:
Icona	Descrizione
	command executed
	command in execution
	command not executed
	cyclic command executed
	cyclic command in execution
	cyclic command not executed
	block executed
	block in execution
	block not executed

By pressing the button refresh you can see in real-time which is the command in execution in that specific time.
## Maximum values
This function allows you to analyze for each place the maximum values of torque curves acquired during testing. Select from the menu Test » Maximum value, or press CTRL + V to access to this window:

Finestra valori massimi
The place or places to be analyzed can be selected in the list visible in the upper left of the window itself. Immediately below it is necessary to activate the boxes Clockwise/Counter-Clockwise to display its curves.
In form it displays three graphs and respectively starting from the top:
- graph of the maximum values;
- graph of errors in contacs;
- graph of the temperature detected in the oven/climatic chamber .
The curves displayed in the first graph are affected by the following options:
- All: graph of the maximum values of all the acquired curves also for error;
- Only acquisitions: graph of the maximum values of the curves only acquired in automatic mode.
A more detailed analysis can also be performed by changing the options for degrees that allow you to include in the calculation only a few curves or even part of them:
- Starting degrees: start value acquisition ;
- Ending degrees: end value acquisition;
- Starting variance: degrees that are discarded for exclude peaks when rotation start;
- Ending variance: degrees to be discarded at the end of each curve for exclude peaks if you hit the limit.
Every time you change one of these values must be selected Update to run the calculations again. The other buttons on the form are:
- Save: save the graph of maximum values as JPEG;
- Export: export the maximum values detected as a text file ;
- Print: displays the print preview of the graphs;
- Exit: close the form.
### Edit the scale of the cycles
The X axis of the graph of the torque values gives the number of cycles, which can be modified in the following manner:
- click on the graph with the right mouse button;
- in the popup menu select select scale and then blocks / steps to view the subdivisions according to the blocks of the program otherwise a number from 1 to 10 representing splitter maximum number of cycles envisaged in the program:

Selezione scala cicli asse X grafico valori massimi
## Leakage tests
This function displays a list of all the leakage tests performed during testing. Select from the menu Test » leakage, or press CTRL + T to access to this window:

Elenco delle prove di tenuta
To view the list of tests, select a place from the list in the upper left of the window. For each test include the following information:
Step: information block / command;
Cycle: number of current cycle of block running;
Total: total cycles performed since the beginning of the test;
Date/Time: date and time of acquisition;
AT: room temperature (inside the oven/climatic chamber );
P.(N): pressure exerted on the rod of the component;
P.(mbar): Pressure testing of the leakage applied from the machine ATEQ ;
Leakage value: leakage value detected by the machine;
Result: result assigned by the test program;
Data: data read from ATEQ machine.
As shown in the image above, the evidence of the magnet are back on a green background, while the other on light blu background. The values must be colored red in the case of a negative result.
the Form displays three graphs and respectively starting from the top:
- diagram of leakage values : maximum leakage values detected;
- magnet errors drawing : for each magnet test with a negative result, the value increases by one;
- temperature diagram.
In the first two diagrams you can be displayed more or less curves according to the number of selected places. To close the form, press Exit .
## Result
This function can access a summary window with all the data of the test and assign a result to the entire test as well and to each individual place. The results given are saved in the archive and can be included in the search functions of the tests.
Select from the menu Test » Result or press CTRL + E to access to the following window:

Finestra "Risultati di collaudo"
For each place listed in the list, shows the following information:
- Cycles executed: total number of cycles performed (can also be less than the total expected if the place has been interrupted);
- Peak L.(Nm) : maximum value of torque counterclockwise;
- Peak R.(Nm) : maximum value of torque clockwise;
- Torque error : number of rotations in which the torque exceeded the linit;
- Contacts error: number of rotations in which was detected a problem in the contacts;
- Leakage error : number of leakage test failed;
- Magnet error : number of magnet test failed.
- Result : result assigned by operator.
To assign at the same time to all components the same result, press Select all , then fill the field Component result and press Update .By pressing Invert selection can be easily selected all components except the one currently selected.
To export all the information displayed press Export and enter the name of the file to be created. The data will be exported in text format separated by tabs.
Press Confirm to save any results assigned otherwise Exit to close without saving the changes.
You cannot change the result of the tests re-opened from the archive

## Exclude a place
During the execution of a test you can exclude a place erasing all data acquired to continue only with the rest place. Select from the menu Places » Exclude and continue than answer YES to the next confirmation message.
The data of a place excluded can not be recovered.

## Saving a place
Is possible to use this function if you want to save in archive the data from place and continue the test only with the rest of places.Select from the menu Place » Save and continue .
A place saved can not be included in the test anymore.

# Test database
This chapter describes the procedures for the search and the opening of the tests that are stored locally or on an external drive (network, USB key).
## Open a saved test
This feature allows you to load and view the tests previously saved in the local database. Select from the menu Archive » Test , or press F9 alternatively press the following button in the toolbar:

As a result the following window appears:

Finestra "Archivio collaudi"
Pressing the button Find will display all the tests saved. You can also search by entering part of the information required in the following fields:
- Number : test number automatically assigned;
- Date from.. to .. : starting date of the test;
- Test Description;
- Supplier/type;
- Model;
- Description;
- Sample/Code/ANC:
- Stamping/Production Date;
- Lot/Traceability;
- Notes;
- Sample Result: Result assigned by the operator.
After viewing the test, select the one you want to see and press Load. The test selected will appear into the list of tests.
To permanently delete the test from the Test Database press Delete and respond YES to the following confirmation message. The delete function is only available after entering the password protection (Refer to the paragraph Password of the Tool chapter).
You can export to a text file the list of tests carried out by pressing the Export List button.
To exit this window without loading a test, press the Exit button.
## Open an external test
This feature allows you to load and view the tests stored on network or other external memory storage. Select from the menu “Archive»External Test” or press ALT + F9 then select the location of the archive:

Selezione percorso dei collaudi esterni
If the path is valid, you will see the same window as the search and selection for testing stored locally. Then consult the previous section for more details.
## Closing a test archived
This function allows you to close a test loaded from the archive and is rapresented with the following icon:

For closing the test it is necessary to select the test you want to close and select from the menu Archive » Close or press the key combination Ctrl + C ; alternatively press the following button in the toolbar:

# Backup test database
Using this feature you can make a copy of the database and all the tests stored on a network drive or external storage. Select from the menu File »Backup to access the following panel:

Utilità di backup
Opening automatically displays the last path used so you need only press the Start and wait for the completion of the copy. The backup can be of two types:
- Backup Complete: copy all the files in the destination and overwrites any files already present (with the same name so inherent to software GasTapsTestSystem);
- Incremental Backup: copy all the files that are not in the destination folder.
With the button Modify is possible to modify the path.
In the backup of the database are also the calibration data of the places.

# Archive components and programs
The paragraphs in this chapter describe the interfaces and functions for the management of the archive components of the standard programs and advanced programs. While there are no special restrictions for viewing, for the management of the archives you have to enter the password as described in the first paragraph Password of tools chapter.
## Components
To enter the archive components select from the menu Archive » Components or press F2 ; alternatively press the following button in the toolbar:
The following window appears:

Finestra "Gestione componenti"
To add a component, you must:
- Press with the mouse on New button.
- Insert the various information in the fields;
- Press Update button to save data.
To edit a component, you must:
- From the list select the component to be modified.
- Modify the information displayed;
- Press Update button to save data.
To delete a component you must
- From the list select the component to be deleted.
- Press Delete button and press Yes to the next confirmation message.
To exit the window press with mouse the Exit button.
The registry component consists of the following information:
##### Supplier/Type
The component manufacturer or type.
##### Model
Identification code of the component.
##### Description
Description if needed
##### Rotation L
Specifies the maximum rotation angle of anticlockwise of the component from 0 ° to 360 °.
##### Rotation R
Specifies the maximum rotation clockwise angle of the component from 0 ° to 360 °.
##### Max torque
It is the maximum acceptable torque value beyond which the machine assumes that there is a failure of the component. The value is expressed in Nm (Newton / meter).
##### Axial contacts
Number of contacts that can change status during the axial movement (press / release). The system can test at most one axial contact.
##### Rotation counters
Number of contacts that can change status several times during the rotation phase left or right. In the system it is possible to test a maximum of three contacts of this type.
##### Pressure
It indicates the nominal pressure that can be made on the component. Put 0 to disable the view and control.
##### Pressure tollerance
Indicates the extent to which values the measured pressure can be considered correct.
## Program
The software GasTapsEnhTestSystem provides two types of programs for the execution of the tests: Standard program e Advanced program. The standard programs can be used to perform the cycles with a single rotation toward the opening and subsequent return to the initial position, while the advanced programs allow you to perform, in the same cycle, more rotations in different positions. Also through the advanced programs you can run leakage testing.
### Standard program
To enter standard program management select menu Archive » Standard programs or press F3; or press the next button in the toolbar:

The following window appears:

Finestra gestione programmi standard
The screen is divided into two parts: the top panel is used to add, modify and delete a program; the bottom panel to add, edit and delete the steps of the selected program.
To add a program you must:
- Press New.
- Type the name of the new program in the “Name” field program;
- Press Update to save data;
- Then proceed as described in the next paragraph for the inclusion of the Steps.
To change the name of a program you must:
- From the list select the program to modify.
- Type the new name in the “Program Name” field.
- Press Update to save data.
To delete a program, you must:
- From the list select the program to be deleted.
- Press Delete and click Yes in the next confirmation message.
#### Step
For each program you have to enter at least one steps that is a phase that is repeated a number of times before proceeding to the command.
To add a step:
- Press New.
- Enter the required data in the text boxes;
- Press Update to save data.
To modify a step:
- Select the step in the list that you want to modify.
- Change the information displayed in the text boxes;
- Press Update to save data.
To delete a step:
- From the list select the step you want to delete.
- Press Delete and Yes in the next confirmation message.
You can also create a copy of a step already existing:
- From the list select the step that you want to make a copy.
- Press Copy.
To close the file, press Exit.
For each step must be inserted the following parameters:
##### Number of cycles
It indicates the number of cycles to be performed. Each cycle is composed by a counter-clockwise rotation and clockwise or vice versa according to the direction of the initial rotation.
##### Rotation begin
It represents the degree of rotation beginning. If non-zero, the start or any restart of the testing will be performed moving the tap up to the set value.
##### End of rotation
It represents the degree in which it stops moving. If you enter the value “0” is made a rotation to the stop; it stops when the value of torque exceeds the limit of 0.6 Nm. If the program includes at least one step to the stop, the maximum rotation of the component is automatically updated. At the beginning of the step during the detection component it will be rotated clockwise or counterclockwise at a reduced speed.
##### Degrees for second
It indicates the speed of rotation.
##### Cycles to read the torque
It indicates after how many cycles it performs a movement torque detection (adjustable in the options of the program as described in the Opzioni Chapter Settings ) in which are stored the values of torque.
##### Axial movements cycles
It indicates after how many cycles is performed axial movement for release and the pressure tap.
##### Oven/climatic chamber T. (°C)
Setpoint temperature of the oven/climatic chamber for the entire duration of the step. The behavior of the oven/climatic chamber in the stages of change in temperature can be modified by the options of the program (Refer to the Opzioni in the Settings chapter).
##### Oven/climatic chamber temperature (degree)
It indicates the oven/climatic chamber temperature to be set for the duration of the step; it is expressed in degrees and may range from 20 to 200.
##### Cycles release
It indicates after how many cycles the tap is released and then pressed to the limit, and left in the position of “Open.”
##### Wait the end of rotation
It indicates the wait time, in seconds, before start moving backwards.
##### Direction of
It indicates the direction of the first changes: Counterclockwise or Clockwise. If you want to test a tap with a central position 0 which provides a rotation clockwise and counterclockwise, before testing you must disable the search starting position as described in Opzioni chapter Settings.
##### Axial contacts
Set this value to “1” to test the axial contact during the pressure and release, or “0” not to perform a test. If enabled, the outcome will be positive if they are detected two changes of state during the pressure and release.
##### Rotation contacts
During the rotation it is possible to test up to a maximum of 3 contacts. Setting a value different from 0 the rotation is successful, if for each contact specified, the system will detect a change of state in both the movement towards the opening for the return to the initial position.
### Advanced program
To enter the editor of advanced programs select menu Archive » Programs advanced or press F4 or simply press the next button in the toolbar:

The following window appears:

Finestra gestione programmi avanzati
Unlike standard programs, the advanced programs are divided into blocks. Each block, repeated for a preset number of cycles, can contain one or more commands selectable among those in the right list.
The management window is divided into three panels: the left is a list of programs, the center is a list of blocks and controls belonging to the selected program, to the right the list of commands can be inserted.
#### Program
To create a new advanced program:
- Right click on the list of programs and select New from the menu that appears;
- Enter the name of the program and press OK .
To rename an advanced program:
Right click on the program you want to rename and choose Rename from the menu that appears.
To create a copy of an existing program:
- Right click on the program you want to copy and choose Copy from the menu that appears;
- In the bottom of the list will appear an exact copy of the selected program with the same name.
To remove an advanced program:
- Right click on the program you want to delete and choose Delete from the menu that appears;
- Press Yes to the next confirmation message.
To import a new advanced program in XML format:
- Click with the right button in the program list and choose Import XML from the menu that appears;
- Enter the file name and press OK.
Export an advanced program to XML:
- Right click on the program you want to export and choose Export XML from the menu that appears;
- Enter the file name and press OK.
To print the listing of a program:
- Right click on the program and choose Print from the menu that appears;
- select the printer and press OK.
#### Block
To create a new block:
- Select the advanced program;
- Click with the right button of the mouse in the central list and choose New Block from the menu that appears;
- Enter a description of the block, the number of cycles, the number indicating how many cycles save a curve, and the maximum torque if other than the default component;
- Press Ok.
It is possible to create a block number equal to 0 cycles in which can be inserted only controls the start and end block (It is inhibited the insertion of the cyclic controls).

To edit a block:
- Click with the right button of the mouse to select the block to edit and choose Edit Block from the menu that appears;
- Edit the parameters in the following window;
- Press Ok to confirm the modifications.
To delete a block:
- Click with the right button Of the mouse to select the block to remove and select Delete block from the menu that appears;
- Press Yes to the next confirmation message.
To copy a block:
Click with the right mouse button to select the block to be copied and choose Copy block from the menu that appears.
You can also create a link to a block. A link creates an identical copy of the selected block and any changes applied to each of the two blocks will also be applied to another. It is also possible to create more than one link for each block.
Click with the right mouse button to select the desired block and choose Create Shortcut of this block from the menu that appears.
#### Command
In the right panel you can see a list of available commands to insert in the blocks.
To add a command, drag it over to the block in which you plan to add. First set if it is a command at a single execution or if it will run at each cycle of the block. Enter the parameters, depending on the command, and press OK to confirm the entry.
The commands to run at the begin of the block, will run only once at the first start or any restart of testing.

To edit a command, select it with the right mouse button and choose Edit command from the menu that appears. Change the parameters and press OK to confirm the changes.
To delete a command, select it with the right mouse button and choose Delete command from the menu that appears. Press Yes to the next confirmation message.
##### List of available commands
In this paragraph are summarized all the implemented commands that can be used in the implementation of advanced programs.

Waiting: it waits for the specified time.
Parameters	Description
Seconds	Waiting time (minimum 0.1)

Confirm Operator: displays a summary screen with the data of torque and the results of the leakage test carried out since the start of testing. The home screen has three buttons:
Parameters	Description
Repeat	Reset the data in the test and restart to the first block
Cancel	Cancel current test and delete all the data acquired
Confirm	Continues with the test

Magnet current OFF: disables the passage of the current to simulate the cooling of the thermocouple.

Magnet current ON: activates the passage of the current to simulate the heating of the thermocouple.

Oven change air flow set: moves the AirFlap present in nozzle air exchange.
Parameters	Description
Position AirFlap	percentage position of AirFlaf (0=close, 100=full open)

Oven door open: Open the door of the oven

Oven close door: Close the door of the oven

Oven/chamber temperature wait: It waits if the oven temperature is below the minimum value or if it is above the maximum value set.
Parameters	Description
Temp. minimum	temperature minimum value
Temp. maximum	temperature maximum value

Oven regulate temperature: set up the temperature of setpoint of the oven.
Parameters	Description
Temperature	setpoint temperature in °C

Oven ventilation adjust: set the speed of ventilation.
Parameters	Description
Speed Ventilation	percentage rate of ventilation (0 = off, 100 = maximum)

If the additional resistance heating is active, the ventilation is taken to the maximum anyway

Open Taps outputs : it opens the solenoid valve that close the outputs of the taps.

Close taps outputs : it close the solenoid valve that close the outputs of the taps.

Leakage test : leakage test of components.
Parameters	Description
Program ATEQ	test program to be selected in the machine ATEQ to perform the test (1..4)
Result negative	expected outcome from the machine dell'ATEQ. If the selected test is positive it means there is a leakage

Magnet leak test : It performs the leak test but the result is identified as magnet test.
Parameters	Description
Speed ventilation	percentage rate of ventilation (0 = off, 100 = maximum)

Tap press : advancing the motor to press the rod of the tap.

Tap release: reverses the motor to release the rod of the tap.

Tap rotate: performs the rotation of the motor.
Parameters	Description
Degree rotation	degrees to be performed
Rotation	direction of rotation: clockwise (R), counterclockwise (L)
Speed rotation	speed in degrees per second of rotation
Unlock motor	state of the motor at the end of rotation. If disabled, the motors remains in “traction”

Tap rotate with test contacts : it performs the rotation of the motor and performs the test of the contacts
Parameters	Description
Degree rotation	degrees to be performed
Rotation	direction of rotation: clockwise (R), counterclockwise (L)
Speed rotation	speed in degrees per second of rotation
Unlock motor	state of the motor at the end of rotation. If disabled, the motor remains in “traction”
Pulse contact mov. axial n.1	if enabled at the end of the rotation, the input n. 1 must have read a pulse. It is necessary that before the rotation command there is the command of pressure or release
Pulse contact mov. rotation n.2	number of pulses to be acquired at the end of rotation by the input n. 2
Pulse contact mov. rotation n.3	number of pulses to be acquired at the end of rotation by the input n. 3
Pulse contact mov. rotation n.4	number of pulses to be acquired at the end of rotation by the input n. 4

Tap motor unlock: perfmor the command to unlock the motors.

Tap find zero position: performs a movement of 360 ° for research of 0. The movement stops when the hardware limit kicks in.
Parameters	Description
Rotation	direction of rotation: clockwise (R), counterclockwise (L)
Speed Rotation	speed in degrees per second of rotation
Unlock motor	state of the motor at the end of rotation. If disabled, the motor remains in “traction”

Pressure set: set the pressure of the motors
Parameters	Description
Type execution	set when the command must be executed if : at the beginning of the block , cyclic or at the end of the block
Pressure (bar)	set the pressure to be exerted , express in bar

# Tool
This chapter describes the functions in the Tools menu of the application.
## Install components
This feature allows the user to make axial movements or rotations during the installation of the components or during breaks of active testing. From this panel, you can also access another screen for manual execution of the leak test.
To access the panel select the menu Tools » Install Components or press the F8 ; more simply press the next button in the toolbar:

The following window appears:

On the left there are listed the places present in the system and for each of these are displayed the following information:
Place: place that is updated with each manual rotation performed;
T.L. (Nm): instantaneous values of torque during counterclockwise rotation;
T.R. (Nm): instantaneous values of torque during clockwise rotation;
Press. (N): axial pressure exerted on the component is available only if there is any axial movement, measured in Newton;
Temp (°C): temperature of the oven or of a possible additional thermocouple placed in the component itself, measured in ° C;
Magnet: icon light on or gray that indicates whether or not the passage of current for the simulation of heating of the thermocouple;
Limit: LED that turns red if the input hardware limit detects a twist exceeding 0.6 N;
Input: LEDs corresponding to the inputs that are green if the contact is closed.
In order to rotate it is necessary to select a location by clicking with the mouse in the corresponding key. You can select all the places by pressing the mouse button Select all . Subsequently with the keys Left or Right you rotate with the degree and the speed set. The degree and the speed can be varied without the help of the keyboard using the buttons Up and Down:

Reset button performs the release of the motors while the keys Forward and Back respectively advance and retreat motors.
The features for the leakage test and magnet on/off are available only if a device for doing leakage test is installed. Than you won't see it in the window.

The section “Pressure (bar)” , if there isn't any device to control the pressure this feature won't be available. Than you won't see it in the window.

### Rotation
It is possible to manually rotate the motor, counterclockwise or clockwise with an angle and with a rotation speed variables.
#### Degrees
The rotation can be from 1 to 360 degrees.
#### Speed degrees/second
Speed of rotation to do from 20 to 200 degrees per second.
#### Left
This command start the left rotation with degrees and speed specified.
#### Right
This command start the right rotation with the degrees and speed specified.
#### Reset
This command stops the movement and unlock the motors. (see section Options in chapter SETTINGS).
### Axial movement
It is possible perform manually the axial movement of the motors to verify the correct positioning of the components.
#### Forward
The command pushes forward The motors of the selected places.
#### Backward
The command moves back the motors of the selected places.
To return to the main application, press with the mouse, the button Exit.
### Current to simulate the Thermocouple
To test the magnet operations, you can manually turn on and off the current in the magnets to simulate the heating of the thermocouple.
#### Magnet On
Enable the current in the selected components.
At the end of the form the current is interrupted.

#### Magnet Off
Disable the current in the selected components.
### Pressure (bar)
With this option , available only if the device to regulate the pressure is installed in the system , you can set the pressure (express in bar) of the motors.
### Manual execution of Leakage tests
Press the button Leakage test to enter in the following panel:

Pannello per l'esecuzione manuale delle prove di tenuta
With the buttons Free and Close in the test boxes Gas Exit it is possible open and close the shutter solenoid valve of the taps outputs, that normally at the beginning is open. To execute a test:
- select the position from 1 a 6 with the buttons on the left side;
- Than select the program to execute in the Ateq from 1 to 4;
- Press the button Leakage test and wait the result in the text box RESULT.
If no result are displayed to be shure that the Ateq machine is turned on and ready to work.

## Oven/Climatic chamber Calibration
With this tool it is possible to calibrate the thermocouple inputs used to read the temperature directly on the components and the pressure inputs.
This system does not include additional thermocouple inputs.

## Password
Some of the functions of database management and editing of parameters at startup , are password protected and you must enable them to take some sort of authentication by entering a password.
To enable the password-protected functions, proceed as follows:
select Instruments→Password or press the following button in the toolbar:

insert the password in the windows and press the button Confirm.
To disable the functions (only if enabled):
select Instruments→Password or press the following button in the toolbar:

To change the password :
select Instruments→Password or press the following button in the toolbar:

- Then enter the password in the window that appears and press Change;
- Insert twice your new password in the appropriate text boxes displayed;
- Confirm the change with the key Confirm immediately below the boxes.

Finestra cambio password
# Setting
This chapter describes the interfaces of the operating modes of the system and the graphical display of data.
## Graphic
To enter in the graphic setting select from the menu Setting » Grafic or push the key F10; or push the following key in the toolbar:

As a result you will see the following window

Finestra "Impostazioni grafico"
The panel is divided into two parts: the left panel allows you to add, edit and delete the colors of the selected curves; the panel on the right allows you to change the unit of measure, the display scales, the number of the selected curves in every direction with the function “Worst” and to choose whether to show the degrees in the display of the points.
To add a color in the selected diagram is necessary:
- Press with the mouse, the button New .
- Select with the mouse the button Color ; therefore, will appear the following figure:

Finestra "Colore"
- Choose a color with the mouse and press the button OK ;
- Press the button Update to save the data.
To change a color, you must:
- From the list select the color to change.
- Press with the mouse the button color .
- Choose a color with the mouse (see figure above) and press OK.
- Press Update to save the data.
To delete a color, you must:
- Select, from the list, the color to delete.
- Press with the mouse the button Delete and respond Yes in the next confirmation message.
To exit the window press the mouse button Confirm.
## Options
To enter in the managements of the options , select ftom the menu Program Options or push the key F11.

Windows program option
The windows is divided in three panels: General, standard program and Advanced program. The first panel contain the general options of application, the other two the basic options of the program running.
### General
The options in this panel are for all tests regardless of the running program.
#### Fault detection
##### Maximum numbers of test out of maximum torque range
The user can set the maximum number of diagrams out of range, exceeding the torque, which are automatically saved during testing in addition to those planned. The achievement of the maximum number programmed can interrupt the test and wait or continue without the failed component.
##### Maximum diagrams with errors in contacts
The user can set the maximum number of diagrams with contacts errors, which are automatically saved during testing in addition to those planned. The achievement of the maximum number programmed can interrupt the test and wait or continue without the failed component. With the option Exclude detecting contact the program continues without count them.
##### Maximum number of magnet-on errors
The user can set the maximum number of leak tests with negative results, whether the component or the magnet. The achievement of the maximum number programmed can interrupt the test and wait or continue without the failed component. With the option Exclude leakage detecting the program continues without performing leak testing.
##### Excluded Degree from the limit test
In performing the end limit test you must specify how many degrees, from the beginning and end of the rotation, should be excluded in the torque test limit. Important this option must be set before the start of a test.
##### Action when the maximum limit errors are reached
It indicates the action to take if a component reaches the maximum number of errors in the Torque or in the contacts detection:
- Stop testing: stop testing without any action;
- Stop place: interrupted testing of the tap in error and continues testing the remaining components;
- Exclude and continues: excludes the failed component (losing all data) and continues testing the remaining components.
### Check voltage absence
##### Restart the test when the power come back
Your system, except the oven, is powered by an UPS. When the power fail , the system continue to work , until reach the first instruction of the cicle, (normally at the zero position) , stop the test and wait the power return. By selecting this option, the PC stops the test untill the communication with the oven is in error.The program will wait for the power come back to resume the testing of components.
### Pressure control
##### Stop the test with over-range pressure of 10%
If you want to stop the test while running for “pressure out of range”, just select this option.
### Standard Program
The Options on this panel affect only the Standard Programs.
#### Control of the Oven Temperature
##### Temperature Setpoint
The first two options, if enabled, affect the duration of the test , at every change of set Point, it stops the execution and wait that the temperature of the oven reaches the setpoint established. The first option affects the passage from one cycle cold to a hot cycle, the second instead interacts in passing from one cycle cold to warm. Each option provides a range that can be increased to decrease the wait.
##### Open the door during the cooling
It enable the door opening during the cooling phase.
The option could be ignored if the open door option is not present

##### Use of the additional fan for cooling
If it is enabled , during the cooling phase , turn on the additional fan to speed up the process.
The option could be ignored if the fan is not present

##### Turn on the additional resistor
If it is enabled , during the heating phase , turn on the additional resistor to speed up the heating process. When reached the Set Point temperature less the value set , the resistor is disabled and it is never used until the next heating cicle.
The option could be ignored if the resistor is not present

#### Movements
##### Unlock the motor at the end of motion
If this option is selected, after the rotation, the motor remains free to turn. In performing of the end stop tests it is preferable to leave the motors held by disabling this option to avoid losing the position.
##### Speed of torque detection (degree/second)
You can set the speed of rotation of the component in the torque data logging. The default is 20 degrees / second which allows for about 2 readings for each degree. You can select or the same speed of test or a lower speed. Note: The torque depends on the speed of rotation.
##### Move the motor to find the start position
The user can also choose to run the movement to find the initial position of the component, at the start of test. The search is performed by rotating the component clockwise. Obviously, the component must provide a limit.
##### Stop the movement before the limit
Because after many cycles running at the end of rotation,it canarise problems in the component, you can set how many degrees the rotation is stopped before the rotation limit. By entering a value different than 0, the test of end limit will be executed only during the cycles of torque detection , for all other cicles , teh rotation will be stopped early based on the value entered.
##### Exclude pressure in the return phase
Activating this Option, it is disabled the pressure of the tap during the movement to return to the starting position. The option affects all cycles of testing during which it is programmed to release the valve in the open position.
##### Time necessary to complete the push command
Time necessary to complete the push movement, before to start the rotation phse. The value is in milliseconds. Usually the time is 500 ms , but it is recommended 1000 ms.
### Enhanced Programs
The options in this panel affect only the execution of enhanced programs.
#### Blocks
##### Disable all the comands of the oven/climatic chamber
This option allows to ignore all the commands of the oven/climatic chamber , both setting (setpoint position airflap, ventilation) and the standby temperature.
##### Esxlude waiting
With this option the program ignore all the waiting commands.
##### Turn on additional fan cooling with door open
Se abilitata durante la fase di raffreddamento in concomitanza dell'apertura della porta accende la ventola supplementare per velocizzare il processo. If enabled, during the cooling fase, when the door is open, turn on the fan to speed up the cooling.
The option could be ignored if the fan is not present

##### Turn on the extra heating resistor to reach the set point
If enabled during the phase of Heating , it turn on an extra resistor to reach faster the setpoint. Once the temperature is reached, the resistor is no longer used until the next command that set the oven temperature.
It could be ignored if resistor is not present

### Oven/climatic chamber Options
The working mode of the oven/climatic chamber can be changed from a control panel in the main screen of the program.

Oven/climatic chamber Panel
The oven can works in two modes:Automatic and Manual. To select one or the other option , push the key Auto o Manual and answer Yes to the confirm message.
It's possible to use Manual mode to run tests also without temperature regulation (ambient condition). The oven or climatic chamber can be also turned OFF.

#### Automatic Mode
The oven temperature changes in correspondence to the steps or the commands of the standard test programs or blocks of advanced programs. If the system is supplied with a climatic chamber, also humidity can be regulated.
#### Manual Mode
The temperature and ventilation of the oven remain stable as values set manually by the operator during the execution of the standard programs that provide step at different temperatures or enhanced programs with commands that controls temperature and ventalation. Even the arm to open and to close the door, remains stationary in its current position. In this mode to change the temperature of the oven set the desired setpoint temperature in the field “Temperature set” and the desired setpoint humidity of the climatic chamber in the field “Humidity and gradient set” and press the OK button .
The humidity settings are available only for the climatic chamber

#### Manual regulations for oven accessories
In manual mode, you can make the following adjustments:
- Regulate the internal ventilation;
- Regulate the back air flap position;
- Open or close the door.
To access the panel settings, press the corresponding button of the options and select the button Confirm to apply your changes or the Cancel button to exit.

Finestra "Opzioni forno"
Those options are available only for system with oven.

#### Climatic condition regulation
This paragraph explains the function/settings for manually adjust climatic test condition. Some of this, for example the humidity control, are availables only for climatic chamber.
##### Climatic chamber START and STOP button
With START button it's possible once set up the parameters: temperature setpoint, humidity setpoint, to put the climatic chamber in “RUN” state to reach the desired conditions according also with the gradients.
With STOP button the climatic chamber will stop to maintain the set up conditions.
##### Temperature and gradient set up
Write the new values or use the right arrows to change them and press the APPLY button to confirm.
Gradient is not available for oven devices.

##### Humidity and gradient set up
Write the new values or use the right arrows to change them and press the APPLY button to confirm. Use the left button to ENABLE/DISABLE the humidity control.
Availables only for climatic chambers.

# Events
The program includes a register which stores any errors that may occur. Each fault is signaled to the operator by a message in which they are given an identification number and a brief description of the error. The same information is also stored in a register. Errors that occur during the execution of automatic procedures can not be communicated to the operator via message but are still stored in the registry.
## View
To consult the Events list click with the mouse in the menu File » Events » View or push the button from the toolbar:

Il program display the following panel:

Finestra "Events"
You can find three types of events according to their importance:
- Error
- Notice
- Information
Double-clicking on an event you can view the entire message in the event that the window is not wide enough.
## Deleting
To clear the event log you must select the menu File » Events » Empty and answer Yes to the following confirm message.