$NOME
Manuale Software

MAREL srl - FABRIANO (AN) – Italy
www.marelsrl.com

# Marel TC Test Gas
## Preface
The goal of this document is to help the operator to use the MarelTCTestGas application.

## Introduction
MarelTCTestGas is an application for testing gas hobs safety thermocouples. The software is intended to use with the Marel special bench.
## Interface
The main window of the application is as follow:

Next sections describe in detail all main window components.
### Menu and toolbar
The table shows all the buttons present in the toolbar with the relative function:
Button	Function
	Create new test
	Modify test data
	Start/Continue test
	Pause current test
	Stop/End current test
	Delete current test
	Unload closed/finished test from main screen
	Opens archived tests window
	Opens the software tools window
	Opens the software channels window
	Opens Log viewer
	Opens the software ADMIN tools window only for bench diagnostic
	Reset test TC threshold warning
	Opens software info version-author
	Close application

### Current/Archieved test details

This area show the current active test or archieved details:
Station state : current test state
State	Description
EMPTY	Station is empty. No current test loaded
READY	Test is ready to start for the first time
PAUSE	Test in in pause. Ready to continue
RUNNING	Test is in running state according with cycles Time On, Time OFF and cycles defined
COMPLETED	Test is completed. All the cycles are executed
STOPPED	Test is definitively interrupted by operator. It could not continue
ERROR/ALARM	Current test is in error state. Please check the LOG to verify the problem. Test can continue once the problem is solved after that operator press PLAY again

Components : number of the components in test.
Model type, Supplier, Batch : components details specified by operator for search purpose once archived.
Elapsed time : elapsed time from the beginning.
Total time : test duration according with Time ON, Time OFF and inserted cycles.
Time left: time left until end.
Time ON: cycle warm time (minutes).
Time OFF: cycle cooling time (minutes).
Current cycle : current running cycle.
Total cycles : total cycles of the test.
Status cycle : ON in case of the system is warming the thermocouples, OFF during the time OFF period.
Temperature : setpoint temperature used to manage test fault and TC acquired voltages verifies.
Comp.T : current temperature in TC connection with gas taps component.
Note: additional test notes.
Immediately below, on the right the software show the currently acquired temperature from the system thermocouple

### Test TC details
When there is current defined test or a test is loaded from archive the software shows the lists of the defined thermocouples.

From the list the operator can show/hide the thermocouple diagrams selecting or deselecting the checkbox. Also he can change color with mouse click on coloured rectangle (default is black) on the right. When test is in RUNNING state the software show the last read value for thermocouple.
### Cycle values diagram
In the center of the screen the operator can see the diagram of the current cycle or a different selected already executed.

There are two diagrams: the first on the top is the Temperature diagram. It show the test temperature acquired with the system temperature thermocouple. The upper and lower lines delimit the accepted temperature range to consider the acquired values millivolts good for test results.
The second graphic area show the diagram of the termocouple generated millivolts. The green area delimits the range used to verify generated millivolts. The area in in percentage from the end of the cycle to avoid to take data during the warming phase at the beginning of the cycle. When the mouse is over the graph, a red bar show the selected read and the acquired value are showed in the right: TC is the main value; In the right for each graph the software show the maximum, average and minimum acquired values for the showed diagrams.
For the test with a minimum threshold defined, the software show a red horizontal line to highlight the minimum acceptable read TC value.
With mouse wheel is possible to zoom the graph.

It's normal that at the beginning of new cycle all the area is green. The area will decrease with time elapsed.

### Test toolbar
The second toolbar in middle of the screen must be used for current test functions:

GO FIRST : show the detail of the first cycle.
BACK : select the previous cycle.
NEXT : select the next cycle.
GO LAST : select the last cycle (completed or actual running).
EXPORT : export the data of the selected cycle as CSV file.
MORE INFO : show a new panel with current test details and cycles averages. Please check Test details window paragraph.
RESET ZOOM : restore default diagram settings.
### Cycles list details
When there is a test defined in the right of the screen a list with all executed cycles will be visible:

At the top of the list there is the TC millivolt threshold min value THLD ERR. and below for each cycle the software show the number wit a green or red box. If at the end of the cyce all thermocouples are over the limit, the box will be green otherwise red. The value inside the box is the number and millivolt of the first component with TC value less then threshold.
To go directly to the cycle, click on the number to see graph and details.
The labels will be green without text in case of no errors.

### Create new test
From the main menu bar select New test

to open the test definition panel:

Insert the thermocoples specification:
model type, supplier, batch (production lot etc…).
Insert the test settings:
Components Number : number of the connected thermocouples;
Temperature (°C) : system target setpoint temperature for TC sensors.
Cycle number : number of the cycles to execute.
Time Cycle On (minutes) : duration of the time on step (warming time).
Time Cycle Off (minutes) : duration of the time off step (cooling time).
Threshold min. (mV) : minimum acceptable voltage for goods thermocouples.
Once filled up the fields, confirm with OK. The station state will become READY.
Before confirm verify the calculated test duration according with cycles number, time ON and time OFF values.

Once the test is created it will be automatically loaded at software startup until COMPLETED or STOPPED

### Components installation
Before start a test it's necessary to verify that all thermocouples are correctly positioned and also the system is reading the correct generated millivolts. So operator has to open the settings panel selecting Channels button from menu .
Please refer to channel window paragraph.

### Start test
When station state is READY once created new test, the operator has to close the safety door and after press the button

In case that an error occur during start or the door is not closed, a warning message will be showed and the test will go in ERROR/ALARM otherwise the station will go in RUNNING state.
In case of operator has to change themocouple position or other settings, the test must be switched to PAUSE state

### Pause test
In RUNNING state state press the button

to switch the state in PAUSE. If the software is performing a time ON step, will stop to warm up the thermocouples and also the gas taps if specified during startup.
Test paused can be resumed at any time.

The door will remain locked until the test surface temperature will decrease under safety conditions. The first green segment of the semaphore must light on

### Stop test
In case it's necessary to close the test before the scheduled end, the operator has to press the button

Once pressed the software will stop to acquire data and station will go in STOPPED state.
STOPPED test are saved into the archive but can't be resumed.

STOPPED test are not more automatically loaded at software startup. To see the data the operator must opens it from archive.

### Delete test
In case it's necessary to definitively delete the test before the scheduled end, the operator has to press the button

Once pressed the software will ask the operator to config to discard current test.
DELETED test are saved into the archive but are not visible and can't be loaded.

### Close test
Once the test is COMPLETED or STOPPED or DELETED, to prepare the system for a new test going in EMPTY state, the operator can press the button

### Software test settings
Some system setting can be customized by the operator and are saved to avoid to insert each time a new test is defined. To modify this settings, the operator must open the tools panel pressing the button

The software will show the following panel

Cycle Interval Analysis % : this value define the last time in percent of the total ON period taken as valid to calculate averages and verify thermocouples working parameters. This period is highlighted as green in the graph.
Range temperature control °C : it defines the difference from the target setpoint to consider the data acquired as valid for test. In case that for any reason the temperature is lower or higher than delimited range within Cycle Interval Analysis period, the acquired data are marked as not valid to avoid to recognize as thermocouples fault.
Threshold min TC alarm (mV) : with a test running, if one ore more acquired thermocouples millivolts is lower than this threshold, the system fill start to blink the BLUE lamp to signal a possible TC problem.
### Channels window
During setup phase or during test execution, the operator pressing the button

can open the panel to see the values of all defined system inputs and other system signals

System temparature : the test bench use this central sensor to verify that the system is working properly and also to compare the acquired millivolts of the connected thermocouples..
Auxiliary temperature : in the test bench there is an other additional auxiliary thermocouple input that could be used by operator during installation procedure or for any other purpose. It is not mandatory and could be also disconnected during test phase.
Components voltages: this box contain all the system defined thermocouples inputs : one input for each to read main generated millivolts.
Motor sensors : there are three defined inputs as explained in below table to signal the thermocoule sliding support position :
Signal	Description
FRONT POSITION	GREEN light when is in WARM position (front), GRAY in case of front position sensor is not detected
BACK POSITION	GREEN light when is in COLD position (back), GRAY in case of back position sensor is not detected
OVER COURSE	RED when the system recognize an over course position detected, GRAY in normal working mode

In case of OVER COURSE only manual intervention can restore the normal working mode moving back or front the sliding support

System signals : there are three defined inputs as explained in below table:
Signal	Description
SAFETY BARRIER	YELLOW light when the barrier recognizes a WARNING state that break the automatic slide movement, GRAY in ca se of normal working mode
BYPASS DOOR SENSOR	YELLOW light if bypass is activated, GRAY when bypass is not active.
SAFETY DOOR SENSOR	YELLOW light when the system recognize that the safety door/panel is closed, GRAY when the door/panel sensors are not recognized as closed

BYPASS DOOR SENSOR should be automatically enabled when the test is not running. With a test running the bypass is disabled

Thermocouples position : operator can press the following buttons to move front or back the sliding support:
Move Front: perform an automatic movement to reach the Front position Move Back: perform an automatic movement to reach the back position
Once pressed, the operator has to wait the end of the movement. In case of hardware problems the MOVEMENT TIMEOUT light will become RED. It is possible to retry movements also with MOVEMENT TIMEOUT signal. In case verify if there are obstacles between barriers that inhibits the movement.
### Open log viewer
Problems occurred during software execution are storend into a text file. The content can be managed pressing the button

In the show panel there are the following tools:
Icon	Button	Command
	Empty Log	Delete all recorded events
	Apply	Show only events according with partial text entered in Filter box
	Remove	Remove selected element from list

### Open archieved test
All the executed test are stored into the archive. To view graph and data of a completed test it's necessary to load it from archive. Operator must press the button

and after in the showed panel will be possible to search the test for some inserted data or execution date interval

Click on Search button, select the test from the list end double click on it or press the Load button.
The software will show a new window with the details of the executed test similar to the main windows. The operator could navigate through the cycles and also view test details as for currently running test.
### Test details window
From main window is possible to see the list of executed cycles but the graph and averages of only one cycle at time. To see the averages and minimum acquired values of the thermocouples millivolts the operator must press the button More Info

Once pressed the program shows a new window

Differently from main screen where X axis was the minutes from the start of the cycle, here the X axis represent the number of the cycle. So the two lines are the result of the minimum values and average values (millivolts) sampled in each cycle.
Instead for the first test temperature graph on the top, the two lines represent the min and max in the cycle.
When the mouse is over the graph area, is possible to see the values in the highlighted cycle. The graph can be panned or zoomed with mouse wheel.
Three buttons are available as in the following table:
Button	Function
	export the acquired values into a CSV file (it could be easily opened with Microsoft Excel (TM)) or Libreoffice Calc (TM)
	reset the zoom
Selected cycle	selecting a different cycle before to open this panel, operator can see partial report instead of for all executed cycles. Please check to enable the option
FIRST LAST	If checked the software will report for each component acquired data at the first and at the last cycle
CYCLES INTERVAL	If selected the software will report data by row according with inserted value
	create a print preview of the test report that can be printed out or exported as .pdf choosing the PDF printer

### ADMIN tools window
This panel is intended to use only for diagnostic purpose.

Technic person with machine schematic diagrams can verify input and output sensors and actuators of the test bench.